## Slide 1: J-K Flip-Flop
Joshua Gould
12/5/2018
ECE 09.414 VLSI Design
Dept. of ECE
Henry M. Rowan College of Engineering Rowan University

## Slide 2: Outline
J-K Flip-Flop Overview / Description
Features / Problems
Block Diagram
Truth Table
Master Slave Design
Design Choices
Logical Design
Worst Case Design
Logical Effort, Number of Stages, Delay
Gate Sizes for Optimized Design
Standard Cell Library & Layout Simulations
Conclusion

## Slide 3: Block Diagram

## Slide 4: Truth Table
Inputs |  |  |  | Outputs |  | Action
J | K | CLK | CLR | Q | Q’ | 
0 | 0 | Edge | 0 | Last Q | Last Q’ | Retain State
0 | 1 | Edge | 0 | 0 | 1 | Reset Q
1 | 0 | Edge | 0 | 1 | 0 | Set Q
1 | 1 | Edge | 0 | Last QN | Last Q | Toggle
0 or 1 | 0 or 1 | 0 or 1 | 1 | 0 | 1 | Asynchronously Reset Q
0 or 1 | 0 or 1 | 0 or 1 | 1 | Last Q | Last QN | Illegal State

## Slide 5: JK Flip-Flop Issues
Uncontrolled toggling when clock is high
Minimized features

## Slide 6: Master/Slave Flip-Flop
Two latch stages in a cascaded configuration
Activated with opposite clock phases
Eliminates uncontrolled oscillations since only one stage is active at any given time
Master Latch
Slave Latch

## Slide 7: Master/Slave Flip-Flop
Single flip-flops suffer from “race” timing problems
Race timing occurs if the output Q changes state before the timing pulse of the clock input has time to go “OFF”.
Master Latch
Slave Latch

## Slide 8: Design Overview
POSSIBILITY 1: NAND Logic Gate
  PROS:
    Simple design
    Smallest design area
    Uses simple gates
  CONS:
    Notable output timing errors
    Minimized features
    Limited in pulse width for the clock and inputs

## Slide 9: Design Overview
POSSIBILITY 2: Master-Slave NAND Logic Gate
  PROS:
    Simple design doubled
    Fixes race error
  CONS:
    Uneven design with clear
    Large amount of transistors
    Minimized features (no PRESET)
    Some constraints on the clock pulse width
    Delay on Slave latch (1/2 clock period)

## Slide 10: Design Overview
POSSIBILITY 3: NOR based JK Flip-Flop
  PROS:
    Fixes the SR Latch with the 3 input NANDs so all inputs are allowed.
  CONS:
    Inputs must be stable for some time before clock goes low.
    The output will oscillate continuously until the or one of the input signals goes low
    Larger design area than NAND only (+2 NOR +2 NOT)
    Highest number of transistors required

## Slide 11: Design Overview
POSSIBILITY 2: Master-Slave NAND Logic Gate
    Fixes race error
    Faster than NOR design

## Slide 12: Logic Design

## Slide 13: Transistor Design

## Slide 14: Worst Case Logical Path
J
Q’
CLK
CLK
Q
K

## Slide 15: Latch Delay Calculation
The logical effort of the flip-flop must be characterized in Cadence due to the feedback path on each latch.
Use d = gh + p to find latch parameters

## Slide 16: Latch Delay Calculation
The logical effort of the flip-flop must be characterized in Cadence due to the feedback path on each latch.
Use d = gh + p to find latch parameters

## Slide 17: Latch Delay Calculation
The logical effort of the flip-flop must be characterized in Cadence due to the feedback path on each latch.
Use d = gh + p to find latch parameters

## Slide 18: Latch Delay Calculation
Chart: Fanout (h)
| 0 | 1 | 2
tpd | 212.105 | 261.3 | 297.012
h | g
0 | 212.105
1 | 261.3
2 | 297.012
d = gh+p
= 42.45h + 214.35
g = 42.45
p = 212.105

## Slide 19: Effective Latch Stages & Normalization
Due to its dependence on feedback path, the latch may not be best described by a single stage.
The parasitic delay of the latch was divided by that of a similar-sized inverter.
We'll assign 2 stages to the latch.

## Slide 20: Inverter Delay Calculation
d = gh+p
= 29.55h + 49.9
g = 29.55
p = 49.9
Normalized Average
g = 1
p = 1
Chart: h
| 0 | 1 | 2
tpd | 49.9 | 73.2 | 109
h | g
0 | 49.9
1 | 73.2
2 | 109

## Slide 21: Latch Delay Calculation
Chart: Fanout (h)
| 0 | 1 | 2
tpd | 212.105 | 261.3 | 297.012
h | g
0 | 212.105
1 | 261.3
2 | 297.012
d = gh+p
= 42.45h + 214.35
g = 42.45
p = 212.105
Normalized Average
g = 1.4367 p = 4.2506

## Slide 22: Gate Sizes for Optimized Design
Top Logic
Bottom Logic

## Slide 23: Gate Sizes for Optimized Design
Stage | Size | Width pMOS |  | Width nMOS |  | Length (m)
R, V | 3.00 | 1.8 | 1.8 | 2.7 | 1.8 | 1.5
S | 7.757 | 3.2 | 3.3 | 4.8 | 4.8 | 1.5
T | 15.508 | 8 | 8.1 | 8 | 8.1 | 1.5
U | 46.515 | 18.8 | 18.9 | 28.2 | 28.2 | 1.5
Stage | Size | Width pMOS |  | Width nMOS |  | 
R, V | 3.00 | 1.8 | 1.8 | 2.7 | 1.8 | 1.5
S | 7.757 | 3.2 | 3.3 | 4.8 | 4.8 | 1.5
T | 15.508 | 8 | 8.1 | 8 | 8.1 | 1.5
U | 46.515 | 18.8 | 18.9 | 28.2 | 28.2 | 1.5
R
V
S
W
T
X
U
Y

## Slide 24: Gate Sizes for Optimized Design
Stage | Size | Width pMOS |  | Width nMOS |  | Length (m)
R,V | 3.00 | 1.8 | 1.8 | 2.7 | 1.8 | 1.5
W | 8.52 | 3.6 | 3.6 | 5.4 | 5.4 | 1.5
X | 14.940 | 7.5 | 7.5 | 7.5 | 7.5 | 1.5
Y | 53.074 | 21.2 | 21.3 | 31.8 | 31.8 | 1.5
Stage | Size | Width pMOS |  | Width nMOS |  | 
R,V | 3.00 | 1.8 | 1.8 | 2.7 | 1.8 | 1.5
W | 8.52 | 3.6 | 3.6 | 5.4 | 5.4 | 1.5
X | 14.940 | 7.5 | 7.5 | 7.5 | 7.5 | 1.5
Y | 53.074 | 21.2 | 21.3 | 31.8 | 31.8 | 1.5
R
V
S
W
T
X
U
Y

## Slide 25: Logical Effort, Number of Stages, Delay
Variable | Stage |  |  |  | N = 4
 | 1 | 2 | 3 | 4 | Path
b | 1 | 2 | 1 | 3 | B = 6
g | 5/3 | 1.4367 | 4/3 | 1.4367 | G = 4.5869042
h | 3.276 | 3.8004 | 4.095 | 3.8004 | H = 90/3 = 30
p | 3 | 4.2506 | 2 | 4.2506 | P = 13.5012
 | 5.46 | 5.46 | 5.46 | 5.46 | F = GBH = 825.64276

## Slide 26: Standard Cell Library
R
V
S
W
T
X
U
Y
U
U
R
S
T

## Slide 27: Standard Cell Library
R
V
S
W
T
X
U
Y
Y
U
V
W
X

## Slide 28: Pre-Layout Simulations

## Slide 29: Pre-Layout Simulations
Master and Slave have a delay between each other of half a clock cycle, understandably slowing down output

## Slide 30: Standard Cell Library Extracted Layouts

## Slide 31: Standard Cell Library Simulation “Spectre” Netlist
i 1 nmos 4 29 0 0 " m 1 l 600e-9 w 1.5e-6 "
; nmos4 Instance /N39 = auLvs device Q2
i 2 nmos 9 5 0 0 " m 1 l 600e-9 w 1.5e-6 "
; nmos4 Instance /N36 = auLvs device Q3
i 3 nmos 10 3 0 0 " m 1 l 600e-9 w 1.5e-6 "
; nmos4 Instance /N32 = auLvs device Q4
i 4 nmos 23 22 0 0 " m 1 l 600e-9 w 3e-6 "
; nmos4 Instance /N25 = auLvs device Q5
i 5 nmos 22 30 11 0 " m 1 l 600e-9 w 3e-6 "
; nmos4 Instance /N26 = auLvs device Q6
i 6 nmos 15 28 21 0 " m 1 l 600e-9 w 3e-6 "
; nmos4 Instance /N21 = auLvs device Q7
i 7 nmos 19 12 30 0 " m 1 l 600e-9 w 5.7e-6 "
; nmos4 Instance /N55 = auLvs device Q8
i 8 nmos 0 22 6 0 " m 1 l 600e-9 w 5.7e-6 "
; nmos4 Instance /N34 = auLvs device Q9
i 9 nmos 16 30 0 0 " m 1 l 600e-9 w 3e-6 "
; nmos4 Instance /N33 = auLvs device Q10
i 10 nmos 0 10 16 0 " m 1 l 600e-9 w 3e-6 "
; nmos4 Instance /N53 = auLvs device Q11
i 11 nmos 7 14 8 0 " m 1 l 600e-9 w 2.7e-6 "
; nmos4 Instance /N51 = auLvs device Q12
i 12 nmos 20 3 0 0 " m 1 l 600e-9 w 2.7e-6 "
; nmos4 Instance /N30 = auLvs device Q13
i 13 nmos 21 0 14 0 " m 1 l 600e-9 w 3e-6 "
; nmos4 Instance /N28 = auLvs device Q14
i 14 nmos 0 12 15 0 " m 1 l 600e-9 w 3e-6 "
; nmos4 Instance /N29 = auLvs device Q15
i 15 nmos 2 24 0 0 " m 1 l 600e-9 w 3e-6 "
; nmos4 Instance /N50 = auLvs device Q16
i 16 nmos 0 3 13 0 " m 1 l 600e-9 w 2.7e-6 "
; nmos4 Instance /N27 = auLvs device Q17
i 17 nmos 28 14 2 0 " m 1 l 600e-9 w 3e-6 "
; nmos4 Instance /N22 = auLvs device Q18
i 18 nmos 11 7 0 0 " m 1 l 600e-9 w 3e-6 "
; nmos4 Instance /N54 = auLvs device Q19
i 19 nmos 6 17 19 0 " m 1 l 600e-9 w 5.7e-6 "
; nmos4 Instance /N52 = auLvs device Q20
i 20 nmos 8 9 20 0 " m 1 l 600e-9 w 2.7e-6 "
; nmos4 Instance /N49 = auLvs device Q21
i 21 nmos 13 4 18 0 " m 1 l 600e-9 w 2.7e-6 "
; nmos4 Instance /N31 = auLvs device Q22
i 22 nmos 24 10 23 0 " m 1 l 600e-9 w 3e-6 "
; nmos4 Instance /N48 = auLvs device Q23
i 23 nmos 18 28 17 0 " m 1 l 600e-9 w 2.7e-6 "
t 5 J inputOutput
t 29 K inputOutput
t 28 Q inputOutput
t 14 Q' inputOutput
t 3 CLK inputOutput
t 27 CLR inputOutput
t 22 Qm inputOutput
t 30 Qm' inputOutput
n 1 vdd!
n 0 gnd!
n 2 /net48
n 3 /CLK
n 4 /net014
n 5 /J
n 6 /net53
n 7 /net12
n 8 /net55
n 9 /net013
n 10 /net025
n 11 /net51
n 12 /net0115
n 13 /net58
n 14 /Q'
n 15 /net49
n 16 /net058
n 17 /net9
n 18 /net57
n 19 /net54
n 20 /net56
n 21 /net50
n 22 /Qm
n 23 /net057
n 24 /net030
n 27 /CLR
n 28 /Q
n 29 /K
n 30 /Qm'
; nmos4 Instance /N41 = auLvs device Q0
d nmos D G S B (p D S)
i 0 nmos 12 27 0 0 " m 1 l 600e-9 w 1.5e-6 "
; nmos4 Instance /N40 = auLvs device Q1
; pmos4 Instance /P33 = auLvs device Q24
d pmos D G S B (p D S)
i 24 pmos 12 27 1 1 " m 1 l 600e-9 w 3e-6 "
; pmos4 Instance /P32 = auLvs device Q25
i 25 pmos 4 29 1 1 " m 1 l 600e-9 w 3e-6 "
; pmos4 Instance /P31 = auLvs device Q26
i 26 pmos 9 5 1 1 " m 1 l 600e-9 w 3e-6 "
; pmos4 Instance /P27 = auLvs device Q27
i 27 pmos 24 10 1 1 " m 1 l 600e-9 w 3e-6 "
; pmos4 Instance /P26 = auLvs device Q28
i 28 pmos 24 22 1 1 " m 1 l 600e-9 w 3e-6 "
; pmos4 Instance /P25 = auLvs device Q29
i 29 pmos 1 30 0 1 " m 1 l 600e-9 w 3e-6 "
; pmos4 Instance /P28 = auLvs device Q30
i 30 pmos 10 3 1 1 " m 1 l 600e-9 w 3e-6 "
; pmos4 Instance /P17 = auLvs device Q31
i 31 pmos 22 30 1 1 " m 1 l 600e-9 w 3e-6 "
; pmos4 Instance /P15 = auLvs device Q32
i 32 pmos 22 7 1 1 " m 1 l 600e-9 w 3e-6 "
; pmos4 Instance /P44 = auLvs device Q33
i 33 pmos 1 22 30 1 " m 1 l 600e-9 w 3.9e-6 "
; pmos4 Instance /P43 = auLvs device Q34
i 34 pmos 1 17 30 1 " m 1 l 600e-9 w 3.9e-6 "
; pmos4 Instance /P12 = auLvs device Q35
i 35 pmos 1 12 30 1 " m 1 l 600e-9 w 3.9e-6 "
; pmos4 Instance /P40 = auLvs device Q36
i 36 pmos 7 14 1 1 " m 1 l 600e-9 w 1.8e-6 "
; pmos4 Instance /P39 = auLvs device Q37
i 37 pmos 7 3 1 1 " m 1 l 600e-9 w 1.8e-6 "
; pmos4 Instance /P9 = auLvs device Q38
i 38 pmos 7 9 1 1 " m 1 l 600e-9 w 1.8e-6 "
; pmos4 Instance /P21 = auLvs device Q39
i 39 pmos 28 24 1 1 " m 1 l 600e-9 w 3e-6 "
; pmos4 Instance /P22 = auLvs device Q40
i 40 pmos 28 14 1 1 " m 1 l 600e-9 w 3e-6 "
; pmos4 Instance /P20 = auLvs device Q41
i 41 pmos 1 12 14 1 " m 1 l 600e-9 w 3e-6 "
; pmos4 Instance /P41 = auLvs device Q42
i 42 pmos 1 3 17 1 " m 1 l 600e-9 w 1.8e-6 "
; pmos4 Instance /P36 = auLvs device Q43
i 43 pmos 1 4 17 1 " m 1 l 600e-9 w 1.8e-6 "
; pmos4 Instance /P42 = auLvs device Q44
i 44 pmos 1 28 17 1 " m 1 l 600e-9 w 1.8e-6 "
; pmos4 Instance /P18 = auLvs device Q45
i 45 pmos 1 0 14 1 " m 1 l 600e-9 w 3e-6 "
; pmos4 Instance /P19 = auLvs device Q46
i 46 pmos 1 28 14 1 " m 1 l 600e-9 w 3e-6 "
; pmos4 Instance /P23 = auLvs device Q47
i 47 pmos 1 10 0 1 " m 1 l 600e-9 w 3e-6 "
t 0 gnd! global
t 1 vdd! global

## Slide 32: Standard Cell Library Simulation Input / Output Waveforms

## Slide 33: Snap-together Standard Cells Circuit Layout

## Slide 34: Snap-together Standard Cells Simulation Input / Output Waveform
[INSERT WHEN CADENCE WORKS]

## Slide 35: Delay Comparison Logical Effort vs. Spectre
[Insert proper image when Cadence is back up]

## Slide 36: Questions?