## Slide 1: J-K Flip-Flop
Joshua Gould
12/11/2018
ECE 09.414 VLSI Design
Dept. of ECE
Henry M. Rowan College of Engineering Rowan University

## Slide 2: Outline
Block Diagram
Truth Table
Basic Flip-Flop / Issues
Master Slave Design
Designs & Choice
Logical Design
Transistor Design
Worst Case Design
Logical Effort, Number of Stages, Delay
Gate Sizes for Optimized Design
Delay Comparisons
Conclusion & Improvements

## Slide 3: Block Diagram

## Slide 4: Truth Table
Inputs |  |  |  | Outputs |  | Action
J | K | CLK | CLR | Q | Q’ | 
0 | 0 | Fall-Edge | 1 | Last Q | Last Q’ | Retain State
0 | 1 | Fall-Edge | 1 | 0 | 1 | Reset Q
1 | 0 | Fall-Edge | 1 | 1 | 0 | Set Q
1 | 1 | Fall-Edge | 1 | Last Q’ | Last Q | Toggle
0 or 1 | 0 or 1 | 0 or 1 | 0 | 0 | 1 | Asynchronously Reset Q
0 or 1 | 0 or 1 | 0 or 1 | 1 | 1 | 1 | Illegal State

## Slide 5: JK Flip-Flop Issues
Uncontrolled toggling when clock is high
Minimized features

## Slide 6: Master/Slave Flip-Flop
Solves this “race” timing problem with a fast clock
Race timing occurs if the output Q changes state before the timing pulse of the clock input has time to go “OFF”.
Master Latch
Slave Latch

## Slide 7: Master/Slave Flip-Flop
Two latch stages in a cascaded configuration
Activated with opposite clock phases
Eliminates uncontrolled oscillations since only one stage is active at any given time
Master Latch
Slave Latch

## Slide 8: Design Overview
POSSIBILITY 1: NAND Logic Gate
  PROS:
    Simple design
    Smallest design area
    Uses simple gates
  CONS:
    Notable output timing errors
    Minimized features
    Limited in pulse width for the clock and inputs

## Slide 9: Design Overview
POSSIBILITY 2: Master-Slave NAND Logic Gate
  PROS:
    Simple design doubled
    Fixes race error
  CONS:
    Uneven design with clear
    Large amount of transistors
    Minimized features (no PRESET)
    Some constraints on the clock pulse width
    Delay on Slave latch (1/2 clock period)

## Slide 10: Design Overview
POSSIBILITY 3 Continuous JK Flip-Flop
  PROS:
    Fixes the SR Latch with the 3 input NANDs so all inputs are allowed.
  CONS:
    Inputs must be stable for some time before clock goes low.
    The output will oscillate continuously until the or one of the input signals goes low
    Larger design area than NAND only (+2 NOR +2 NOT)
    Highest number of transistors required

## Slide 11: Design Overview Comparison
Design | Major Concern | # of Transistors | # of stages
1 - Simple | Run time error | 22 | 2
2 - MastSlav | Higher Delay/ Clock limitation | 46 | 4
3 - NOR | Inputs must be stable | 54 | 5

## Slide 12: Design Choice
POSSIBILITY 2: Master-Slave NAND Logic Gate
    Fixes race error
    Faster than NOR design

## Slide 13: Logic Design

## Slide 14: Logic Design

## Slide 15: Logic Design

## Slide 16: Transistor Design

## Slide 17
3C

## Slide 18
3C

## Slide 19: Transistor Design

## Slide 21
90C

## Slide 23: Transistor Design

## Slide 24: Worst Case Logical Path

## Slide 25: Worst Case Logical Path

## Slide 26: Worst Case Logical Path

## Slide 27: Worst Case Logical Path
J
Q’
CLK
CLK
Q
K

## Slide 28: Latch Delay Calculation
The logical effort of the flip-flop must be characterized in Cadence due to the feedback path on each latch.
Use d = gh + p to find latch parameters

## Slide 29: Latch Delay Calculation
The logical effort of the flip-flop must be characterized in Cadence due to the feedback path on each latch.
Use d = gh + p to find latch parameters

## Slide 30: Latch Delay Calculation
The logical effort of the flip-flop must be characterized in Cadence due to the feedback path on each latch.
Use d = gh + p to find latch parameters

## Slide 31: Effective Latch Stages & Normalization
Due to its dependence on feedback path, the latch may not be best described by a single stage.
The parasitic delay of the latch was divided by that of a similar-sized inverter.
Assigned 2 stages to the latch.

## Slide 32: Latch Delay Calculation
Chart: Fanout (h)
| 0 | 1 | 2
tpd | 212.105 | 261.3 | 297.012
h | g
0 | 212.105
1 | 261.3
2 | 297.012
d = gh+p
= 42.45h + 214.35
g = 42.45
p = 212.105

## Slide 33: Inverter Delay Calculation
d = gh+p
= 29.55h + 49.9
g = 29.55
p = 49.9
Normalized Average
g = 1
p = 1
Chart: h
| 0 | 1 | 2
tpd | 49.9 | 73.2 | 109
h | g
0 | 49.9
1 | 73.2
2 | 109

## Slide 34: Latch Delay Calculation
Chart: Fanout (h)
| 0 | 1 | 2
tpd | 212.105 | 261.3 | 297.012
h | g
0 | 212.105
1 | 261.3
2 | 297.012
d = gh+p
= 42.45h + 214.35
g = 42.45
p = 212.105
Normalized Average
g = 1.4367 p = 4.2506

## Slide 35: Gate Sizes for Optimized Design
Top Logic
Bottom Logic

## Slide 36: Gate Sizes for Optimized Design
Stage | Size | Width pMOS |  | Width nMOS |  | Length (m)
R,V | 3.00 | 1.8 | 1.8 | 2.7 | 1.8 | 1.5
S | 7.757 | 3.2 | 3.3 | 4.8 | 4.8 | 1.5
T | 15.508 | 8 | 8.1 | 8 | 8.1 | 1.5
U | 46.515 | 18.8 | 18.9 | 28.2 | 28.2 | 1.5
Stage | Size | Width pMOS |  | Width nMOS |  | 
R,V | 3.00 | 1.8 | 1.8 | 2.7 | 1.8 | 1.5
S | 7.757 | 3.2 | 3.3 | 4.8 | 4.8 | 1.5
T | 15.508 | 8 | 8.1 | 8 | 8.1 | 1.5
U | 46.515 | 18.8 | 18.9 | 28.2 | 28.2 | 1.5
R
V
S
W
T
X
U
Y

## Slide 37: Gate Sizes for Optimized Design
Stage | Size | Width pMOS |  | Width nMOS |  | Length (m)
R,V | 3.00 | 1.8 | 1.8 | 2.7 | 1.8 | 1.5
W | 8.52 | 3.6 | 3.6 | 5.4 | 5.4 | 1.5
X | 14.940 | 7.5 | 7.5 | 7.5 | 7.5 | 1.5
Y | 53.074 | 21.2 | 21.3 | 31.8 | 31.8 | 1.5
Stage | Size | Width pMOS |  | Width nMOS |  | 
R,V | 3.00 | 1.8 | 1.8 | 2.7 | 1.8 | 1.5
W | 8.52 | 3.6 | 3.6 | 5.4 | 5.4 | 1.5
X | 14.940 | 7.5 | 7.5 | 7.5 | 7.5 | 1.5
Y | 53.074 | 21.2 | 21.3 | 31.8 | 31.8 | 1.5
R
V
S
W
T
X
U
Y

## Slide 38: Logical Effort, Number of Stages, Delay
Variable | Stage |  |  |  | N = 4
 | 1 | 2 | 3 | 4 | Path
b | 1 | 1.51 | 1 | 1.5619 | B = 5.0719
g | 1.6667 | 1.4367 | 1.3334 | 1.4367 | G = 4.5869042
h | 3.276 | 3.8004 | 4.095 | 3.8004 | H = 90/3 = 30
p | 3 | 4.2506 | 2 | 4.2506 | P = 13.5012
 | 5.46 | 5.46 | 5.46 | 5.46 | F = GBH = 697.93

## Slide 39: Logical Effort, Number of Stages, Delay
Variable | Stage |  |  |  | N = 4
 | 1 | 2 | 3 | 4 | Path
b | 1 | 1.51 | 1 | 1.5619 | B = 5.0719
g | 1.6667 | 1.4367 | 1.3334 | 1.4367 | G = 4.5869042
h | 3.276 | 3.8004 | 4.095 | 3.8004 | H = 90/3 = 30
p | 3 | 4.2506 | 2 | 4.2506 | P = 13.5012
 | 5.46 | 5.46 | 5.46 | 5.46 | F = GBH = 697.93

## Slide 40: Standard Cell Library
R
V
S
W
T
X
U
Y
U
U
R
S
T

## Slide 41: Standard Cell Library

## Slide 42: Standard Cell Library
R
V
S
W
T
X
U
Y
Y
INV
V
W
X

## Slide 44: Pre-Layout Simulations
Consider MASTER to SLAVE Delay
Consider clock speed
Size of gates vary the input to output and can alter inputs as the bottom path is slower than the top.
Master and Slave have a delay between each other of a half clock cycle (clock pulse width)
4n Clock period behavior

## Slide 46: Pre-Layout Simulations
Falling Clock Q Rising Delay = tpdr = 2.5132 ns
Slave output rising time is about 0.8932 ns behind the master

## Slide 47: Pre-Layout Simulations
Falling Clock Q Falling Delay = tpdf = 3.1342 ns

## Slide 48: Pre-Layout Simulations
Simulated Slave Output Delay = 2.8237 ns where clock cycle is 4 ns

## Slide 49: Pre-Layout Simulations
Simulated Slave Output Delay = 2.8237 ns where clock cycle is 4 ns
Recall the delay 2.0437 ns

## Slide 50: JK Flip-Flop Layout Design

## Slide 51
65.55 X 90.75
196.65 x 272.25

## Slide 53: Spectre Netlist
N69 (net43 CLR 0 0) ami06N w=1.5u l=600n as=2.25e-12 ad=2.25e-12 ps=6u \
pd=6u m=1 region=sat
N68 (net18 K 0 0) ami06N w=1.5u l=600n as=2.25e-12 ad=2.25e-12 ps=6u pd=6u \
m=1 region=sat
N67 (net27 J 0 0) ami06N w=1.5u l=600n as=2.25e-12 ad=2.25e-12 ps=6u pd=6u \
m=1 region=sat
N0 (net57 CLK 0 0) ami06N w=1.5u l=600n as=2.25e-12 ad=2.25e-12 ps=6u \
pd=6u m=1 region=sat
N66 (Q\' Q net129 0) ami06N w=31.8u l=1.5u as=4.77e-11 ad=4.77e-11 \
ps=66.6u pd=66.6u m=1 region=sat
N65 (net129 net059 net130 0) ami06N w=31.8u l=1.5u as=4.77e-11 ad=4.77e-11 \
ps=66.6u pd=66.6u m=1 region=sat
N64 (net130 net43 0 0) ami06N w=31.8u l=1.5u as=4.77e-11 ad=4.77e-11 \
ps=66.6u pd=66.6u m=1 region=sat
N4 (net33 CLK net139 0) ami06N w=2.7u l=600n as=4.05e-12 ad=4.05e-12 \
ps=8.4u pd=8.4u m=1 region=sat
N71 (net0133 net055 0 0) ami06N w=28.2u l=1.5u as=4.23e-11 ad=4.23e-11 \
ps=59.4u pd=59.4u m=1 region=sat
N3 (net136 net33 0 0) ami06N w=4.8u l=1.5u as=7.2e-12 ad=7.2e-12 ps=12.6u \
pd=12.6u m=1 region=sat
N61 (net133 Qm\' 0 0) ami06N w=7.5u l=1.5u as=1.125e-11 ad=1.125e-11 \
ps=18.0u pd=18.0u m=1 region=sat
N8 (net140 Q\' 0 0) ami06N w=2.7u l=600n as=4.05e-12 ad=4.05e-12 ps=8.4u \
pd=8.4u m=1 region=sat
N7 (net139 net27 net140 0) ami06N w=2.7u l=600n as=4.05e-12 ad=4.05e-12 \
ps=8.4u pd=8.4u m=1 region=sat
N63 (Qm\' Qm net131 0) ami06N w=5.4u l=600n as=8.1e-12 ad=8.1e-12 ps=13.8u \
pd=13.8u m=1 region=sat
N5 (net131 net32 net132 0) ami06N w=5.4u l=600n as=8.1e-12 ad=8.1e-12 \
ps=13.8u pd=13.8u m=1 region=sat
N6 (net132 net43 0 0) ami06N w=5.4u l=600n as=8.1e-12 ad=8.1e-12 ps=13.8u \
pd=13.8u m=1 region=sat
N58 (net32 CLK net138 0) ami06N w=2.7u l=1.5u as=4.05e-12 ad=4.05e-12 \
ps=8.4u pd=8.4u m=1 region=sat
N57 (net138 Q net137 0) ami06N w=2.7u l=1.5u as=4.05e-12 ad=4.05e-12 \
ps=8.4u pd=8.4u m=1 region=sat
N62 (net059 net57 net133 0) ami06N w=7.5u l=1.5u as=1.125e-11 ad=1.125e-11 \
ps=18.0u pd=18.0u m=1 region=sat
N70 (Q Q\' net0133 0) ami06N w=28.2u l=1.5u as=4.23e-11 ad=4.23e-11 \
ps=59.4u pd=59.4u m=1 region=sat
N59 (net135 Qm 0 0) ami06N w=8.1u l=1.5u as=1.215e-11 ad=1.215e-11 \
ps=19.2u pd=19.2u m=1 region=sat
N1 (Qm Qm\' net136 0) ami06N w=4.8u l=1.5u as=7.2e-12 ad=7.2e-12 ps=12.6u \
pd=12.6u m=1 region=sat
N56 (net137 net18 0 0) ami06N w=2.7u l=1.5u as=4.05e-12 ad=4.05e-12 \
ps=8.4u pd=8.4u m=1 region=sat
N60 (net055 net57 net135 0) ami06N w=8.1u l=1.5u as=1.215e-11 ad=1.215e-11 \
ps=19.2u pd=19.2u m=1 region=sat
P62 (net43 CLR vdd! vdd!) ami06P w=3u l=600n as=4.5e-12 ad=4.5e-12 ps=9u \
pd=9u m=1 region=sat
P61 (net18 K vdd! vdd!) ami06P w=3u l=600n as=4.5e-12 ad=4.5e-12 ps=9u \
pd=9u m=1 region=sat
P60 (net27 J vdd! vdd!) ami06P w=3u l=600n as=4.5e-12 ad=4.5e-12 ps=9u \
pd=9u m=1 region=sat
P59 (net57 CLK vdd! vdd!) ami06P w=3u l=600n as=4.5e-12 ad=4.5e-12 ps=9u \
pd=9u m=1 region=sat
P58 (Q\' net059 vdd! vdd!) ami06P w=21.3u l=1.5u as=3.195e-11 ad=3.195e-11 \
ps=45.6u pd=45.6u m=1 region=sat
P57 (Q\' Q vdd! vdd!) ami06P w=21.3u l=1.5u as=3.195e-11 ad=3.195e-11 \
ps=45.6u pd=45.6u m=1 region=sat
P56 (Q\' net43 vdd! vdd!) ami06P w=21.3u l=1.5u as=3.195e-11 ad=3.195e-11 \
ps=45.6u pd=45.6u m=1 region=sat
P6 (Qm\' net43 vdd! vdd!) ami06P w=3.6u l=600n as=5.4e-12 ad=5.4e-12 \
ps=10.2u pd=10.2u m=1 region=sat
P7 (net33 CLK vdd! vdd!) ami06P w=1.8u l=600n as=2.7e-12 ad=2.7e-12 \
ps=6.6u pd=6.6u m=1 region=sat
P8 (net33 Q\' vdd! vdd!) ami06P w=1.8u l=600n as=2.7e-12 ad=2.7e-12 \
ps=6.6u pd=6.6u m=1 region=sat
P5 (net33 net27 vdd! vdd!) ami06P w=1.8u l=600n as=2.7e-12 ad=2.7e-12 \
ps=6.6u pd=6.6u m=1 region=sat
P54 (Qm\' net32 vdd! vdd!) ami06P w=3.6u l=600n as=5.4e-12 ad=5.4e-12 \
ps=10.2u pd=10.2u m=1 region=sat
P51 (Q net055 vdd! vdd!) ami06P w=18.9u l=1.5u as=2.835e-11 ad=2.835e-11 \
ps=40.8u pd=40.8u m=1 region=sat
P47 (net32 CLK vdd! vdd!) ami06P w=1.8u l=1.5u as=2.7e-12 ad=2.7e-12 \
ps=6.6u pd=6.6u m=1 region=sat
P46 (net32 net18 vdd! vdd!) ami06P w=1.8u l=1.5u as=2.7e-12 ad=2.7e-12 \
ps=6.6u pd=6.6u m=1 region=sat
P53 (net059 Qm\' vdd! vdd!) ami06P w=7.5u l=1.5u as=1.125e-11 ad=1.125e-11 \
ps=18.0u pd=18.0u m=1 region=sat
P45 (net32 Q vdd! vdd!) ami06P w=1.8u l=1.5u as=2.7e-12 ad=2.7e-12 ps=6.6u \
pd=6.6u m=1 region=sat
P3 (Qm net33 vdd! vdd!) ami06P w=3.3u l=1.5u as=4.95e-12 ad=4.95e-12 \
ps=9.6u pd=9.6u m=1 region=sat
P0 (Qm Qm\' vdd! vdd!) ami06P w=3.3u l=1.5u as=4.95e-12 ad=4.95e-12 \
ps=9.6u pd=9.6u m=1 region=sat
P52 (net059 net57 vdd! vdd!) ami06P w=7.5u l=1.5u as=1.125e-11 \
ad=1.125e-11 ps=18.0u pd=18.0u m=1 region=sat
P50 (Q Q\' vdd! vdd!) ami06P w=18.9u l=1.5u as=2.835e-11 ad=2.835e-11 \
ps=40.8u pd=40.8u m=1 region=sat
P2 (net055 Qm vdd! vdd!) ami06P w=8.1u l=1.5u as=1.215e-11 ad=1.215e-11 \
ps=19.2u pd=19.2u m=1 region=sat
P55 (Qm\' Qm vdd! vdd!) ami06P w=3.6u l=600n as=5.4e-12 ad=5.4e-12 \
ps=10.2u pd=10.2u m=1 region=sat
P48 (net055 net57 vdd! vdd!) ami06P w=8.1u l=1.5u as=1.215e-11 \
ad=1.215e-11 ps=19.2u pd=19.2u m=1 region=sat
include "./_graphical_stimuli.scs"
simulatorOptions options reltol=1e-3 vabstol=1e-6 iabstol=1e-12 temp=27 \
tnom=27 scalem=1.0 scale=1.0 gmin=1e-12 rforce=1 maxnotes=5 maxwarns=5 \
digits=5 cols=80 pivrel=1e-3 sensfile="../psf/sens.output" \
checklimitdest=psf
tran tran stop=380n errpreset=moderate write="spectre.ic" \
writefinal="spectre.fc" annotate=status maxiters=5
finalTimeOP info what=oppoint where=rawfile
modelParameter info what=models where=rawfile
element info what=inst where=rawfile
outputParameter info what=output where=rawfile
designParamVals info what=parameters where=rawfile
primitives info what=primitives where=rawfile
subckts info what=subckts where=rawfile
saveOptions options save=allpub

## Slide 54: Post-Layout Simulation Input / Output Waveform
Falling Clock Q Rising Delay = tpdr = 2.5132 ns
Slave output rising time is about 0.8932 ns behind the master

## Slide 55: Post-Layout Simulation Input / Output Waveform
Falling Clock Q Rising Delay = tpdr = 2.5132 ns
Slave output rising time is about 0.8932 ns behind the master

## Slide 56: Post-Layout Simulation Input / Output Waveform
Falling Clock Q falling Delay = tpdf = 2.5132 ns

## Slide 57: Post-Layout Simulation Input / Output Waveform
Propagation Delay = tpd = 2.3011 ns where clock cycle is 4 ns
Compared to Simulated Slave Output Delay = 2.8237 ns
And the logical effort calculation of 2.0437 ns

## Slide 58: Delay Comparison
 | Time | Units
Layout | 2.3011 | ns
Schematic | 2.8237 | ns
Calculation | 2.0437 | ns
%DIFF | Percent
Layout | -12.87%
Schematic | -39%
Lay -> Schem | +26.13%

## Slide 59: Delay Comparison
 | Time | Units
Layout | 2.3011 | ns
Schematic | 2.8237 | ns
Calculation | 2.0437 | ns
%DIFF | Percent
Layout | -12.87%
Schematic | -39%
Lay -> Schem | +26.13%

## Slide 60: Delay Comparison
 | Time | Units
Layout | 2.3011 | ns
Schematic | 2.8237 | ns
Calculation | 2.0437 | ns
%DIFF | Percent
Layout | -12.87%
Schematic | -39%
Lay -> Schem | +26.13%

## Slide 61: Conclusion
JK Flip-Flops are limited by the speed of the clock.
If the clock is slow, the system delay will increase by the pulse width
At a fast-enough clock, the system will present timing issues other then race
There is a balance between clock and system performance / delay
System delay can be improved with decreased transistors, faster clock, output stabilization, or layout design compacting.